## Slide 1: Linux RS-485 DLL User Manual

## Slide 2: 1. Performance Test
Test Environment
  Ubuntu Linux 22.04.3
  Raspberry Pi 3B – 32bit Bullseye (23.05.03 Release)
Test Method
  Sending the API 1000 times in a row
  Repeat the process above for 10 times
  Calculate the average time
Test Result
  The transfer speed in Linux is almost same as the transfer speed in Windows

## Slide 3: 2. How to Download
Visit the FASTECH website.
https://fastech-motions.com

## Slide 4: 2. How to Download
2) Click ‘DOWNLOADS – Search Downloads’

## Slide 5: 2. How to Download
3) Search “linux” and download RS-485 Linux Library

## Slide 6: 3. Linux System Setting – Serial Port
Serial Port setting required to communicate with FASTECH products.
1. Activate the Serial Port according to the OS configuration methods.
Example) For Raspberry Pi OS, set as follows > sudo raspi-config > Interface Options > Login Shell(No) > Serial Port Enable(Yes)
2. Check the connected serial port. (Serial Port name varies depending on connection method and environment)
> ls –l /dev/tty*
3. Permission is required to use a serial port. (Choose the options below)
3-1. Use root privileges when running a program
> sudo ./test
3-2. Grant execute permission to serial port
> sudo chmod 666 /dev/ttyUSB0

## Slide 7: 3. Linux System Setting – Library Setting
The structure of the ‘Include’ directory containing the FASTECH library is as follows.
1. Copy the ‘Include’ directory to your project path.
2. Copy FASTECH shared library files and symbolic links to the Linux shared library directory.
sudo cp –df ./libEziMOTIONPlusR.so* /usr/local/lib
sudo ldconfig

## Slide 8: 4. How to Use RS-485 Library
Unlike the Windows library, the Linux library sets the Port ID during the connection. When using the API, Slaves are identified by Port ID.
Port ID

## Slide 9: 4. How to Use RS-485 Library
To use the FASTECH API, you need to include FAS_EziMOTIONPlusR.h first.
2) When building a program, you need to import the FASTECH library first.