## Slide 1: Linux Ethernet DLL User Manual

## Slide 2: 1. Performance test
Test environment
  Ubuntu Linux 22.04.3
  Raspberry Pi 3B – 32bit Bullseye (23.05.03 Release)
Test Method
  Sending the API 1000 times in a row
  Repeat the process above for 10 times
  Calculate the average time
Test Result
  The transfer speed in Linux is almost same as the transfer speed in Windows

## Slide 3: 2. How to Download
Visit the FASTECH website.
https://fastech-motions.com

## Slide 4: 2. How to Download
2) Click ‘DOWNLOADS – Search Downloads’

## Slide 5: 2. How to Download
3) Search “linux” and download Ethernet Linux Library

## Slide 6: 3. Linux System Setting – Static IP
You need to set a static IP address for the Ethernet Port that shares the gateway with FASTECH products.
1. Open the OS network configuration file in Terminal.
> ‘sudo nano /etc/dhcpcd.conf’ or ‘sudo nano /etc/network/interfaces’ (It may vary depending on your system.)
2. After the last line of the network configuration file, type the following statement. (It may vary depending on your system.)
(Please modify the blue text to match your PC settings.)
interface eth0 (Address for Ethernet communication with Fastech products)
static ip_address=192.168.0.100 (Static IP address that doesn’t cause conflicts)
static routers=192.168.0.1
3. After saving and exiting the file, reboot the system.

## Slide 7: 3. Linux System Setting – Library Setting
The structure of the ‘Include’ directory containing the FASTECH library is as follows.
1) Copy the ‘Include’ directory to your project path.
2) Copy FASTECH shared library files and symbolic links to the Linux shared library directory.
sudo cp –df ./libEziMOTIONPlusE.so* /usr/local/lib
sudo ldconfig

## Slide 8: 4. How to Use Ethernet Library
To use the FASTECH API, you need to include EziMOTIONPlusE.h first.
2) When building a program, you need to import the FASTECH library first.